## Slide 1
Programme: B.Tech in Computer Science and Engineering
Course Code: BCSE497J
Protocol-Gated Three-Class EEG Classification of Mental State: Healthy, Depression, and Stress
B.Tech Fall Semester Project Review 2 (Project ID: 20701UG01)
STUDENT TEAM MEMBERS
• Saksham Singh (23BDS0028)
• Anish Mukul Ringe (23BDS0082)
• Akshat Agarwal (23BKT0003)
FACULTY SUPERVISOR
Prof. Dhivyaa C. R. School of Computer Science & Engineering (SCOPE)
Vellore Institute of Technology, Vellore

## Slide 2
BCSE497J - Project - I
Approval Mail From Guide
22-08-2026
SCOPE
2
Official approval obtained for Project Scope, Objectives, and System Design before Review 2

## Slide 3
BCSE497J - Project - I
Project Aim, Background & Motivation
22-08-2026
SCOPE
3
PROJECT AIM
To build a robust, scientifically honest, and reproducible three-class EEG classifier over {Healthy, Depression, Stress} using frontal channels, strictly evaluated under subject-disjoint and device-disjoint conditions to actively expose and bypass data-leakage and hardware confounds common in published literature.
CLINICAL BACKGROUND
Subjective Diagnostic Paradigm: Current diagnosis relies heavily on self-reports (PHQ-9, GAD-7) and subjective clinical interviews [56, 62].
Scaling Bottleneck: High mental health caseloads limit the availability of specialists, creating an urgent need for automated, low-cost screening [56, 62].
Scalability of Frontal EEG: Direct, non-invasive measurement of cortical activity; few frontal electrodes enable rapid, general-practitioner deployment [56, 63].
SCIENTIFIC REPRODUCIBILITY CRISIS
The 99% Accuracy Trap: Academic papers report near-perfect EEG classifier performance, but methods reveal critical data leaks [56, 63].
Temporal Data Leakage: Splitting overlapping windows randomly places identical subject impedance on both sides of train/test folds [56, 64].
Hardware Confounding: Multi-class EEG studies pool single-class corpora, allowing deep models to identify hardware signatures instead of brain pathology [57, 65].

## Slide 4
BCSE497J - Project - I
Technical Project Abstract
22-08-2026
SCOPE
4
EXECUTIVE TECHNICAL SUMMARY
Unification of 6 Corpora: Unified six public EEG corpora (MODMA, Mumtaz, SAM40, Cognitive Load, EEGMAT, BRMH) onto a highly standardized representation of six frontal channels (Fp1, Fp2, F7, F3, F4, F8) at 128 Hz in 4s windows, generating 15,728 clean EEG segments across 108 subjects [57, 65].
Unmasking the Device Confound: Proven that multi-class pooling silently enables models to identify recording amplifiers rather than neurophysiology. A non-EEG device-only classifier scores 0.6267 three-class accuracy, and stripping this signature via Riemannian re-centering collapses performance to 0.3255 (chance level is 0.3333) [57, 58].
Protocol-Gated Factorization: Proposed a dual-head model where a shared EEGNet backbone feeds two masked binary heads. The emitted label is selected by one bit of metadata (resting vs. task) known at acquisition, avoiding a flat softmax and preventing hardware memorization [58, 110].
Hierarchical Router & Specialists: Designed an autonomous hierarchical router-plus-specialist model achieving 0.6820 three-class accuracy, representing the ONLY architecture out of 36 configurations to successfully clear the non-EEG device shortcut (+0.0553) [58, 113].
Robust Clinical Transfer: Established device-disjoint depression transfer (MODMA <-> Mumtaz) achieving 0.8675 / 0.8438 accuracy across two independent split draws (permutation null: 0.3998). Cross-device stress transfer is shown to be inert [58, 114].

## Slide 5
BCSE497J - Project - I
Literature Review: EEG Affective Classifiers
22-08-2026
SCOPE
5
Recent EEG-based affective computing studies and their key methodological boundaries (Max 2 slides)
Paper / Study | Objective | Methodology | Pros / Cons | Findings / Accuracy
Wang et al. (2021) [47] MODMA Dataset | Detect major depression from frontal resting EEG | Intrinsic Time-scale Decomposition (ITD) + Temporal Conv Net (TCN) | Pros: Effective temporal learning Cons: Single-corpus training with high generalization risk | 86.87% Accuracy on MDD versus healthy controls
Hamatta et al. (2022) [48] Multimodal Data | Improve physiological stress classification | Genetic Algorithm + ECNN-LSTM on EEG, PPG, GSR signals | Pros: Extremely high classification accuracy Cons: Multi-sensor complex setup; limited feature analysis | 99.9% Accuracy on pooled physiological stress data
Singh et al. (2024) [45] EEG & Audio | Develop multimodal framework for depression | ResKAN Encoder + Cross-Attention using EEG & Audio data | Pros: Deep multimodal interaction Cons: High computational latency; highly dependent on audio | 99.0% Multimodal 98.0% EEG-alone accuracy
Lloyd et al. (2024) [49] SAM40 Dataset | Evaluate pre-trained foundation model on stress | Neuro-GPT Fine-Tuning with SVM on preprocessed EEG data | Pros: Introduces large foundation pretraining Cons: Subjective stress labels; massive electrode mismatch | 74.4% Accuracy on 40-subject stress task
EEG ML/DL Survey (2025) [50] Comprehensive Review | Review SOTA EEG depression detection models | Comprehensive survey of CNN, RNN, LSTM, and Hybrid models | Pros: Clear landscape audit Cons: Highlights that SOTA relies on binary & single-corpus tests | Concludes that domain shift and multi-class are unaddressed

## Slide 6
BCSE497J - Project - I
Key Gaps in Current Academic Literature
22-08-2026
SCOPE
6
Gap 1: Dataset Confounding (Hardware Bias)
Multi-class EEG papers pool distinct single-class corpora, which silently couples pathology labels with recording amplifiers. An SVM or CNN given ONLY recording device identity scores 0.6267 accuracy, completely bypassing neurophysiology [82, 83].
Gap 2: Unsound Evaluation (Data Leakage)
Studies routinely employ random train/test splits on overlapping signal windows. This leaks a subject's unique temporal and spatial skull impedance to both sides of the split, inflating a simple model's performance from 0.6256 to 0.9393 [84].
Gap 3: Lack of Empirical Controls
Papers assert deep-learning superiority without benchmarking against untrained/random networks. When tested, an untrained random backbone matches or exceeds trained networks on stress tasks (0.6390 vs 0.5884 trial AUC) [84].
Gap 4: Unmeasured Generalization Limits
Cross-device clinical transfer is rarely evaluated. When dropped into device-disjoint scenarios (unseen amplifiers), conventional flat multi-class models collapse completely to chance levels [85, 91].
Gap 5: Anxiety Under-served in EEG
No raw EEG dataset co-registers anxiety alongside stress and depression. On the single-protocol clinical cohort (BRMH, n=527) where all four classes coexist, anxiety is the least recoverable class, with recall at 0.146–0.178 [85].

## Slide 7
BCSE497J - Project - I
Objectives, SDGs, and Expected Outcomes
22-08-2026
SCOPE
7
OBJECTIVES
O1. Unify Heterogeneous Corpora: Project 6 raw EEG datasets onto canonical 6 frontal channels (Fp1, Fp2, F7, F3, F4, F8) at 128 Hz in 4s windows with zero NaNs [86, 88].
O2. Quantify Confound Baseline: Measure the non-EEG device-only baseline (0.6267 shortcut) before deep learning architecture exploration [86, 88].
O3. Establish Rigorous Ceilings: Enforce 5-fold subject-grouped CV with out-of-fold evaluations for honest per-task baseline [86, 88].
O4. Algorithm Innovation: Design a multi-class architecture that strictly beats the 0.6267 device-only shortcut [86, 88].
O5. Device-Disjoint Transfer: Measure performance cross-device under a label-permutation null to prove true physiological generalization [87, 88].
O6. Serialized Deployment: Deliver a serialised predictor script (predict.py) for clinical triage screening [87, 89].
SUSTAINABLE DEVELOPMENT GOALS (SDGs)
SDG 3: Good Health and Well-being Sub-target 3.4: By 2030, reduce by one third premature mortality from non-communicable diseases through prevention and treatment and promote mental health and well-being. Project Contribution: Establishes a highly accessible, objective, low-cost screening pipeline using front-facing wearable EEG headsets (6 electrodes) to support population-scale early screening [8, 103, 104].
EXPECTED OUTCOMES
• Scopus Conference/Journal Submission of the peer-reviewed 15-page specification.
• Fully operational three-class screening model clearing the 0.6267 hardware baseline.
• Validated device-disjoint transfer benchmarks (MODMA <-> Mumtaz).
• Open-source command-line tool for front-end EEG triage and decision-support.

## Slide 8
BCSE497J - Project - I
Framework / System Architecture Block Diagram
22-08-2026
SCOPE
8
Functional architecture of the proposed Protocol-Gated Dual-Head Classifier (Gated on Acquisition Metadata)
INPUT EEG DATA [6 Channels × 512 Samples] (4.0s @ 128 Hz) Frontal Projection Fp1, Fp2, F7, F3, F4, F8
SHARED BACKBONE EEGNet CNN Trunk (1,200 Parameters) Produces 256-D Latent Feature Embedding Space
PROTOCOL GATE Reads 1-Bit Tag [Resting vs. Task] (Acquisition metadata known before recording)
Depression Head (Resting-State Specialist) Threshold p_dep >= theta_dep Outputs: Depression | Healthy
Stress Head (Cognitive Task Specialist) Threshold p_str >= theta_str Outputs: Stress | Healthy
ARCHITECTURAL PRINCIPLES
• Masked Multi-Task Loss: Every segment is assigned targets (y_dep, y_str) in {-1, 0, 1}^2. A value of -1 masks unsupervisable channels, zeroing loss gradients from irrelevant tasks. Trunk consumes all data simultaneously without gradient leakage [23, 110].
• Refusal of Flat Softmax: Competing models map targets to a single nominal softmax. However, because no single corpus contains all classes, this forces hardware classification. Protocol-gated decoupling completely bypasses this risk [110, 111].

## Slide 9
BCSE497J - Project - I
System Requirements: Functional (FR1 - FR14)
22-08-2026
SCOPE
9
DATA PIPELINE (FR1 - FR5)
FR1: Multi-corpus Ingestion - Read raw EDF, MAT, CSV, NPY, recovering subject IDs cleanly from filenames [95].
FR2: Channel & Rate Harmonisation - Standardise channels to 6 frontal electrodes (Fp1, Fp2, F7, F3, F4, F8) at 128 Hz [96].
FR3: Bandpass & Notch Filter - Apply zero-phase Butterworth bandpass (0.5-45 Hz, order 8) and 50 Hz notch [96].
FR4: Segment Windowing - Segment EEG into 4s windows (512 samples) with 50% overlap [96].
FR5: Variance Gating - Rejects electrode artifact spikes with variance > k*median (k=10.0) [96].
MODELING & FEATURES (FR6 - FR9)
FR6: Feature Extraction - Support two featuresets: v1 81-col (RBP, DE, FAA, Spectral Entropy) and v2 273-col (PLV, Hjorth, 1/f slope) [96].
FR7: Masked Labeling - Label segments with masked binary sentinel (-1) for invalid supervision tasks [97].
FR8: Model Training - Train SVM, RF, XGBoost, and deep networks (EEGNet, TSception, LSTM) with GRL [97].
FR9: Gated Inference - Route raw EEG through protocol-gated heads (Resting -> MDD; Task -> Stress) [97].
RIGOR & DEPLOYMENT (FR10 - FR14)
FR10: Subject-Grouped splits - Enforce subject-disjoint training folds to prevent intra-subject temporal leakage [97].
FR11: Baselines & Controls - Report every accuracy alongside majority, device shortcut, and permutation null [97].
FR12: Threshold Tuning - Optimize balanced accuracy cutoffs on inner validation, transferring as rank quantiles [97].
FR13: JSON Result Persistence - Output OOF predictions and JSON parameters for strict auditable verification [97].
FR14: Deployable predictor - CLI prediction script accepting (6, N) arrays, executing serialised models [97].

## Slide 10
BCSE497J - Project - I
System Modules & Technical Specifications
22-08-2026
SCOPE
10
CORE FUNCTIONAL MODULES
Module 1: Ingestion & Invariant Check - Reads MAT, EDF, CSV. Parses subject IDs with 100% accuracy and asserts strict zero-NaN tolerance on matrix output [96, 116].
Module 2: Preservative Preprocessing - Applies 0.5-45Hz bandpass and notch. Executes global z-scoring across the (6, 512) matrix, preserving absolute Frontal Alpha Asymmetry ratios [67, 96].
Module 3: Dual-Generation Feature Engine - Computes Handcrafted v1 (81-D) spectral, v2 (273-D) temporal (Hjorth, slope), and Riemannian tangent space projections [72, 96, 97].
Module 4: Masked Multi-Task Model Engine - Trains classical and deep models using a masked BCE loss, zeroing out irrelevant task gradients from disjoint corpora [97, 110].
Module 5: Prediction & Serialized Deployment - Aggregates window-level probabilities and applies rank-quantile decision thresholds for clinical screening decision-support [97, 117].
TECHNICAL SOFTWARE ENVIRONMENT
To guarantee NFR1 (strict reproducibility), library versions are strictly pinned. In particular, scikit-learn is pinned to 1.9.0 to eliminate version-dependent GroupKFold tie-breaking discrepancies [107, 108].
Operating System | Linux (Arch), kernel 7.2.x / CUDA Docker
Programming Language | Python 3.11+
Numerical & Data Stack | NumPy 2.4.6, pandas, SciPy, h5py
Machine Learning Stack | scikit-learn 1.9.0 (pinned), XGBoost
Deep Learning Stack | TensorFlow 2.21.0 (Keras 3.14), PyTorch 2.13
EEG Signal Libraries | MNE-Python, pyriemann 0.12

## Slide 11
BCSE497J - Project - I
Results: The Confounding Trap and Spurious Splits
22-08-2026
SCOPE
11
THE SPURIOUS SPLIT ILLUSION
A simple model trained with a naive random split reports an inflated, near-perfect accuracy that fails completely in clinical deployment [15, 31, 32].
• The Leakage Mechanism: Overlapping 4.0-second windows from the same subject land on both sides of a random split fold. The model memorizes individual temporal/spatial skull impedance profiles, reporting inflated scores without learning any pathology [31, 32]. • Deep Model Inflation: Single-split variance adds an average of +0.21 AUC inflation to deep models, while classical models remain stable [32].
RANDOM SPLIT ACCURACY 0.9393 Spurious Memorization
SUBJECT-GROUPED CV 0.6256 Honest Generalization
THE HARDWARE CONFOUND TRAP
Because no public corpus contains more than two target classes, naive dataset pooling silently equates diagnostic classes with recording devices [57, 83].
• The Confound Mechanism: All 3,599 depression segments belong to MODMA; all 5,497 stress segments belong to SAM40. A flat three-class model learns the amplifier noise spectral signatures, scoring 0.6256 accuracy (SVM) which trails the non-EEG device-only ID shortcut of 0.6267 [13, 28]. • Proof via Covariance Re-centering: Removing device-specific covariance manifolds via Riemannian re-centering collapses SVM and deep model accuracies to 0.3255 (pure chance), proving that flat models contain no generalizable neurophysiology [13, 29].
DEVICE-ONLY SHORTCUT 0.6267 Zero Neurophysiology
RIEMANNIAN COV COLLAPSE 0.3255 Pure Chance (Chance=0.33)

## Slide 12
BCSE497J - Project - I
Results: Hierarchical Router Clears the Shortcut
22-08-2026
SCOPE
12
THE TWO-STAGE HIERARCHICAL MODEL
Since the protocol-gated dual-head model is selected via external metadata (having no flat 3-class score), we built an autonomous hierarchical counterpart. It predicts the routing gate instead of reading it, providing a direct 3-class baseline [25, 112].
• Stage 1 Router (v2 Features): Uses the comprehensive 273-column featureset to classify recording corpus / hardware protocol, achieving a routing gate accuracy of 0.9703 [25, 113].
• Stage 2 Specialists (v1 Features): Restricts input to the 81-column featureset to prevent overfitting on small subject cohorts, classifying pathology within the routed domain [25, 114].
• Dynamic Guard Rails: Specialist heads deploy only if they outperform the inner cross-validation majority class baseline; otherwise, they fall back to corpus majority [25, 113, 114].
• The Breakthrough Score: Achieves 0.6820 three-class accuracy, representing the ONLY model of 36 evaluated architectures to clear the 0.6267 non-EEG device-shortcut floor (+0.0553) [26].
3-CLASS ACCURACY COMPARISON
Evaluated Architecture | 3-Ch Acc | vs. Shortcut
Theoretical Chance Baseline | 0.3333 | -0.2934
Majority Class Baseline (Always Healthy) | 0.4217 | -0.2050
Device ID Shortcut (Non-EEG Floor) | 0.6267 | --
Best Flat Model (RBF SVM on 81 Feat) | 0.6256 | -0.0011
Hierarchical (v1 Router + v1 Specialist) | 0.6486 | +0.0219
Hierarchical (v2 Router + v1 Specialist) | 0.6820 | +0.0553

## Slide 13
BCSE497J - Project - I
Results: Cross-Device Clinical Generalization Bounds
22-08-2026
SCOPE
13
ROBUST DEPRESSION TRANSFER
Our protocol-gated depression head demonstrates true physiological transfer across hardware and geographical populations [14, 33].
• Robust Biological Generalization: Over two independent split draws, MODMA to Mumtaz scores 0.8675 and 0.8438 subject accuracy, which is massively above the permutation null. This is a highly defensible cross-device result surviving different amplifiers and country demographics [14, 33]. • Reverse Viability: The reverse direction Mumtaz to MODMA yields 0.6638 and 0.6667, also clearing the permutation null threshold [14, 33].
MODMA -> MUMTAZ 0.8675 / 0.8438 Null Threshold: 0.3998
MUMTAZ -> MODMA 0.6638 / 0.6667 Null Threshold: 0.5431
INERT CROSS-DEVICE STRESS
In stark contrast to depression, cognitive stress models show zero physiological generalizability in device-disjoint evaluations [14, 33].
• The Transfer Failure: Moving from SAM40+CogLoad training corpora to the held-out EEGMAT amplifier yields accuracies (0.4167 / 0.5000 / 0.5833) that are statistically indistinguishable from the 0.5556 label-permutation null [14, 33]. • Methodological Takeaway: Cognitive stress signatures are highly hardware-dependent or subject-specific. Claims of generalizable stress classifiers in cross-device settings are invalid on this data, representing an inert physiological signal [14, 33].
TRANSFER ACC (L=1) 0.4167 / 0.5000 Null Threshold: 0.5556
TRANSFER ACC (L=0) 0.5833 Null Threshold: 0.5556

## Slide 14
BCSE497J - Project - I
Results: Random Backbone Controls & Channel Density
22-08-2026
SCOPE
14
THE UNTRAINED BACKBONE CONTROL
Deep models are rarely benchmarked against untrained equivalents. When evaluated, an untrained, random-weight EEGNet backbone matches or beats trained models on stress tasks [15, 34].
• Stress / SAM40 [Trial AUC]: Completely untrained random backbone gets 0.6390, whereas the trained model reaches only 0.5884 (Permutation null is 0.5053) [34].
• Stress / CogLoad [Within-Sub AUC]: Untrained backbone reaches 0.9381, while the trained network trails at 0.8690 (Permutation null is 0.5992) [34].
• The Parameter Mechanism: 33,287 of 34,487 (96.5%) network parameters reside inside the classification heads rather than the backbone. On small-sample cohorts, the untrained backbone functions as a random projection classifier, preserving high-dimensional representations without risk of overfitting [34].
CHANNEL DENSITY INVERTED-U EFFECT
Sweeping channel density reveals that 'more data' is not always better. Higher sensor density overfits on modest academic cohorts [35, 37].
6 Channels (Frontal Standard) -> 0.6667 Subject AUC Establishes a solid, generalizable screening standard utilizing only frontal electrodes [35].
32 Channels (Optimal Density) -> 0.7371 Subject AUC The peak performance point of the Inverted-U curve, balancing spatial representation and parameter constraint [35].
128 Channels (Full HydroCel) -> 0.6279 Subject AUC Complete overfitting collapse. Performance drops below the 6-channel frontal baseline due to statistical dimensional starvation on modest clinical cohorts [35, 37].

## Slide 15
BCSE497J - Project - I
Important Negative Findings and Limitations
22-08-2026
SCOPE
15
LIMITATIONS, SOFTWARE ERRORS, & DISCLAIMERS
• Strict Diagnostic Triage Disclaimer: This system is NOT designed or clinically validated for medical diagnosis. It is positioned strictly as a decision-support, low-cost screening triage aid for clinicians [19, 98, 104].
• Stress Generalization Limits: The cognitive stress specialist head lacks cross-device generalization. When evaluated on the held-out EEGMAT dataset, performance matches untrained random backbones and is bounded by the permutation null threshold [34, 40].
• Sample Size Boundedness: Modest cohort sizes (15–61 subjects) cause single-split accuracies to swing by over 10.8% across splits, meaning small differences are statistically unresolvable without multiple split draws [32, 40].
• Anxiety Separability Gap: Anxiety has poor separation from depression under a single protocol (BRMH, n=527), showing a per-disorder recall of only 0.146–0.178. Demographics alone match combined EEG accuracy [35, 40].
• The Legacy Sampling Defect: 15% of segments in the legacy SAM40 dataset retain an unpatched decimation defect. This was intentionally left unpatched to ensure perfect reproducibility across the 36 evaluated architectures [39, 40].
• Silent Software Failures Exposed: The methodological audit identified three critical bugs: tuning on F1 caused models to predict all-positive; absolute transfer thresholds failed cross-device; and degenerate thresholds produced spurious balanced accuracy rankings [32, 40].

## Slide 16
BCSE497J - Project - I
Conclusion and Future Work
22-08-2026
SCOPE
16
PROJECT KEY TAKEAWAYS
• Protocols Dominate Architecture: In EEG classification, the evaluation protocol is the dominant source of reported accuracy. Random splits over overlapping windows inflate performance from 0.6256 to 0.9393 [15, 41].
• Factorization Beats Softmax: Decoupling three-way nominal decisions into binary specialists (gated on protocol metadata or routed hierarchically) is the only mathematically defensible way to utilize pooled single-amplifier datasets [12, 13, 40].
• Explicit Geometry Beats Deep Learning: Riemannian tangent-space projections and covariance geometry outperform deep models on small clinical cohorts [37, 41].
• Sensor Density Inverted-U: Peak performance occurs at 32 channels. High-density montages (128 channels) overfit rapidly [35, 41].
FUTURE RESEARCH WORK
Ramped-alpha DANN: Implement domain-adversarial neural networks (DANN) with an annealed alpha schedule (0 -> 1) rather than a fixed coefficient. This stabilizes the initial backbone representations before applying the gradient-reversal penalty [42].
Continuous Psychometric scoring: Transition from binary diagnostic classification to continuous regression of psychometric scores (PHQ-9 and GAD-7) to model fine-grained, intermediate distress states [42].
Multimodal Expansion: Incorporate and synchronize 6.2 GB of MODMA event-related potential (ERP) and audio recordings currently on disk, moving beyond EEG-only models to multimodal architectures [42].
Bayesian Hyperparameter Sweeps: Conduct nested Bayesian optimization sweeps to establish whether the deep-learning performance gaps relative to Riemannian baselines persist [42].

## Slide 17
BCSE497J - Project - I
Academic References
22-08-2026
SCOPE
17
ACADEMIC REFERENCES (IEEE FORMAT)
[1] R. J. Davidson, "Anterior electrophysiological asymmetries, emotion, and depression: Conceptual and methodological conundrums," Psychophysiology, Vol. 35, No. 5, (1998), pp. 607–614.
[2] H. Cai, Y. Gao, S. Sun et al., "MODMA dataset: A multi-modal open dataset for mental-disorder analysis," Scientific Data, Vol. 9, (2022), Art. no. 178.
[3] V. J. Lawhern, A. J. Solon, N. R. Waytowich et al., "EEGNet: A compact convolutional neural network for EEG-based brain–computer interfaces," Journal of Neural Engineering, Vol. 15, No. 5, (2018).
[4] A. Barachant, S. Bonnet, M. Congedo, and C. Jutten, "Multiclass brain–computer interface classification by Riemannian geometry," IEEE Transactions on Biomedical Engineering, Vol. 59, No. 4, (2012), pp. 920–928.
[5] P. Zanini, M. Congedo, C. Jutten, S. Said, and Y. Berthoumieu, "Transfer learning: A Riemannian geometry framework with applications to brain–computer interfaces," IEEE TBME, Vol. 65, No. 5, (2018), pp. 1107–1116.
[6] S. Kapoor and A. Narayanan, "Leakage and the reproducibility crisis in machine-learning-based science," Patterns, Vol. 4, No. 9, (2023), Art. no. 100804.
[7] W. Mumtaz, S. S. A. Ali, M. A. M. Yasin, and A. S. Malik, "A machine learning framework involving EEG-based functional connectivity to diagnose major depressive disorder (MDD)," Medical & Biological Engineering & Computing, Vol. 56, No. 2, (2018), pp. 233–246.